## Slide 1: 3D Printing in the RoboDojo
Captain Matt Audette
Aug 2017
mraudett@nps.edu

## Slide 2: Topics Covered
History
Basic Overview
Types of printers
Ultimaker 2
Printing on the Ultimaker 2
Best practices

## Slide 3: History
“Additive manufacturing”
“Rapid prototyping”
First developed in the mid 80s
2007- first commercial system under $10,000, “RepRap” movement and open source
2009- first commercially available kits
BfB RapMan and MakerBot “Replicator”

## Slide 4: Uses
Rapid prototyping
Complex, non-machinable shapes
Less material used
Tools and internals printed all at once (eg. ratchets)
Deals in bits and bytes
Small batch manufacturing
“Hyper Local Manufacturing”
Societal impacts

## Slide 5: Uses

## Slide 6: Uses

## Slide 7: Military Use -Update
Air Force/plastic clips
USMC field testing
  Nibbler
  Osprey ($900,000)
  EOD/innovation challenge
http://www.military.com/daily-news/2016/09/29/marines-conducting-tests-with-3d-printed-munitions.html

## Slide 8: Types of Printers
SLS- Selective Laser Sintering
SLA- Stereolithography
FFF- fused filament fabrication
  FDM- Fused Deposition Modeling

## Slide 9: Selective Laser Sintering
Oldest type
Photoreactive powder and lasers
Large, expensive machines
Messy and difficult to engineer
Only just becoming commercially available
Why? // metal printing Video:
https://www.youtube.com/watch?v=cNGdGC5SCKg

## Slide 10: Stereolithography
Photoreactive resin liquid
High quality prints
  Used my professional prop and model makers
Longer prints vs FFF
More expensive printers, consumables

## Slide 11: Fused Filament Fabrication
Us!
Thermoplastics layered
  “Hot glue gun”
Cheapest printers
Cheapest materials w/ widest variety
  PLA, ABS, rubber, nylon, wood
Lowest quality prints
RepRap movement
Kits
Prusa i3 Kit Printer

## Slide 12: Parts
Extruder
  Single vs dual Update
  Diameters of filament
Motors, fans
Feed mechanism
  Push vs pull
Shroud/enclosure
  With, without
Print bed
  Heated vs non heated
Input port
  Tethered vs nontethered

## Slide 14: Printable Materials
PLA
Lower temperature resistance
Less heat warping
Weaker plastic, more rigid
Greater variety of colors
Higher printing speeds, smaller layers, sharper corners
Cheaper
Hobbyist preferred
ABS
Higher temperature resistance
“Curls” easier, heat warping
Strong plastic, more flexible
Soluble in acetone – “welding”
Somewhat machinable
Slight smell
Requires heated bed
Engineer preferred

## Slide 15: Exotic Materials
Wood
Nylon
Rubber
PET-G
PVA
Sandstone
Clay
Chocolate
Plastic Explosives (LLNL)
Brass/Copper

## Slide 16: Characteristics of 3D Prints
Hollow- infill
  “honeycomb”
Overhangs
  Automatic in Cura

## Slide 17: Printing
Ultimaker 2+
3d Models
G-Code and Cura
Loading files
Printing
Changing Settings
Calibrating the Ultimaker
Changing Materials
Best practices

## Slide 18: Ultimaker 2+
Universally good reviews
  Performance vs cost ($2,000)
Ships assembled
  Prints right out of the box
Stand alone
Reliability/Ease of use
Support
Non-proprietary materials

## Slide 19: Steps to Printing
3D Model
  SolidWorks, SketchUp, Maya, Fusion 360
  Thingiverse
Generate G-Code
  Line by line instructions for printer
  “Slicer” program
  Sometimes proprietary
  Cura for Ultimakers (.stl files)
  Set print settings: layer height, infill, brim/skirt/raft
Send files to the printer
  Tethered, SD card, USB
Watch, adjust, wait

## Slide 20: Print Settings in Cura
Running theme:
  time and material vs quality of print!
  tailor to your specific need!
Layer height:
  smaller = better resolution, more time to print
  .1mm = “normal” resolution, .06mm = “high” resolution
% Infill:
  Higher = stronger print, more material used, more time to print
Model Orientation
Position on bed
Model scale

## Slide 21: Cura
“Slicing software”
Translates 3d models to G-code
Takes .stl files

## Slide 22
Open .stl files
Select Printer
“Save to SD Card”
Scale,
Time to print, Materials
Simple/Advanced
settings
General Tip:
Mouse over for details

## Slide 23
Scale
Notice Changes
“Print head shadow”
Movement Arrows

## Slide 24
Rotate
Snap rings for X, Y, Z axes
Printerhead shadow affect placement
Rotated models snap to print surface

## Slide 25
Mirror
Individual model settings
Views: Solid, Xray, Layers

## Slide 26
Layer Height
.1mm low res
.06mm high res
Infill density
(20% is par)
Support
(Everywhere vs Touching build plate)
Platform Adhesion
-Brim (set width)
-Skirt
-Raft (setings)
Print Sequence
-One at a time vs all at once
Things to change

## Slide 27
Things to not touch
Always enable retraction
Speed (Default is fine)
Enable cooling fans (can change during print)
Experimental

## Slide 28: Skirt vs Raft vs Brim
Skirt
  Outline, does not touch part
  “Primes” extruder before print
  Minimal adhesion, shorter print time, less material
Brim
  Concentric outlines of part
  Touches part
  Middle ground
  Good adhesion (ABS)
Raft
  Platform/latticework
  Stabilize models with narrow footprints
  Maximum time, material, adhesion

## Slide 29: Changing Print Settings
During print: “Print Settings”
Extruder temperature
  ( 210 deg PLA, 250 ABS)
Bed temperature
  ( 60 deg PLA, 100 deg ABS)
Fan speed
Tips:
Personal print log
Observe previous prints
  If the print before yours sucked, yours will too!
  Adjust based off of theirs
Default: don’t touch it unless it needs fixing!

## Slide 30: Adhesion
Hedging bets to make our prints stick
Lots of tools in the toolbox:
  Glue stick
  Painter’s tape
  Awesomely wide masking tape
  White glue (tacky)
  PEI sheets
  Jell-o

## Slide 31: Best Practices
“Test shot” before long prints
  Catan house, earring
“Can I?” vs “Should I?”
  Reinventing wheels that are commercially available
  Right tool for the right job
    Laser cutter
    CNC
    Hardware stuf
  Boxes

## Slide 32: Best Practices
Print models one at a time!
  In Cura
  Faster prints
  Failures in prints means losing part, not all
Model positioning in Cura
  Widest part down
Check your spool!
  Never wrap filament over itself
  Check remaining amount

## Slide 33: Best Practices
Break up complex models
  Higher success rate
  netFabb- free software
Finishing your prints
  Paint/sanding goes a long way
  Primer filler
  Supplement with hardware/other materials
Clean up the printer

## Slide 34: Changing Materials
On printer:

## Slide 35: Calibrating the Ultimaker 2+

## Slide 36: Further Reading/Watching
I Like to Make Stuff: Hobby level tutorials http://www.iliketomakestuff.com/category/3dprinting/
Punished Props: In depth tutorials, blueprints, and finshing how tos: http://punishedprops.com/3d-printing/
Splitting .stl files: http://www.3dprintmd.com/print/split-an-stl-from-the-thingiverse-into-multiple-objects/
Video tutorial: https://www.youtube.com/watch?v=6rostD8O5sg

## Slide 37: References
https://3dprintingindustry.com/3d-printing-basics-free-beginners-guide/history/
http://makezine.com/2016/09/15/myanmars-farmers-are-3d-printing-their-own-tools/
http://makezine.com/2013/10/18/3d-printing-umbilical-cord-clamps-in-haiti/
http://www.technologist.eu/the-rise-of-open-source-prosthetics/
https://www.nasa.gov/mission_pages/station/research/news/3Dratchet_wrench
http://www.protoparadigm.com/news-updates/the-difference-between-abs-and-pla-for-3d-printing/

## Slide 38: References: Videos
SLA Form 1+ : http://www.iliketomakestuff.com/3d-printing-with-the-form-1-sla-printer/
https://www.facebook.com/MARCORSYSCOM/videos/vb.179229838801763/1482358698488864/?type=2&theater

## Slide 39: Notes
Pull up Thingiverse
Pull up Cura
Printer, study aides, filaments, tools
Start test print
Websites:
  Videos
  Punished Props
  Maker’s Muse
  I Like to Make Stuff